# ELM-IR-126 IR Projector

The IR-126 designed to support camera cover range up to 200m. The IR-126 is operational since 2006 and is used for to assist license plate recognition software.

| Features: |  |
| --- | --- |
| LED Array wavelength | 850 nm |
| Beam Range 850nm: | 150-200 m |
| Viewing angles 2Θ,° | 25 |
| Dimensions | 330*260*56 mm |
| Color | Black or gray |
| Weight | 4 Kg |
| Protection Standard | IP66 |
| Optical Configuration | Groups of 6 high power IR LED with optical lenses, uniform illumination |

| Environmental: |  |
| --- | --- |
| Operating Temperature, Outdoor Equipment: | -35°C to +50°C. |
| Operating Humidity, Outdoor Equipment: | 5% - 100% |
| Power Requirements: | 110 Watt |
| Input voltage | 12 - 24 VDC |
| Accessories |  |
| Mounting bracket Power cable | According to customer requirement 3m |